## Slide 1: Air to Air and Air-Sourced Heat Pump (ASHP)
Helen Howard

## Slide 2: 1955 3 bed mid terrace

## Slide 3: Air to air outdoor unit

## Slide 4: Air to air indoor unit

## Slide 5: Air to air investment
Installation to family room which has high ceiling 01 November 2023 £1,680
One day’s work
Annual maintenance £96
takes a couple of hours
Reason for purchase to test out how much heat I needed with gas switched off.
Can heat or cool – quick acting
Unobtrusive and very cheap to run

## Slide 6: ASHP outdoor unit Daikin

## Slide 7: ASHP pipework behind unit

## Slide 8: ASHP hot water tank

## Slide 9: ASHP investment etc
15 August 2025 installation
£15,730 less £7,500 grant and £300 discount
= £7,930 of which £2,500 cost of changing microbore piping and 5 radiators
2 weeks work by Octopus
Post-installation: excellent follow-up support
There will be annual maintenance cost
Slow acting; I keep it switched on all the time
It is unusual for indoor temp to drop below 16C

## Slide 10: Total Energy low running costs
January 2026 bill £72.43
February 2026 bill £65.62
March 2026 bill £33.68
Tariff: Intelligent Octopus Go for car charger
6.67p per unit for 6 hrs at night 11.30 to 5.30
to charge car and fill batteries, used to run the house all day including heating
(free solar energy when the sky is light)

## Slide 11: Ground Source Heat Pump and Air to Air Heat Pump
Nick Ward

## Slide 12
12kw NIBE ground source heat pump
Installed summer 2017
Replaced oil boiler (no mains gas)
£19k in total
This included £1800 for 500m trench
RHI has more than covered the cost
Heats water as well as radiators
Used October to April
In summer, PV heats water

## Slide 14: Some issues
… Fitting it all in!
Had some problems shortly after 7-year warranty expired
Finding competent (and competitive) service engineers
Is annual servicing really needed?
  Yes for warranty
  Thereafter??
Negotiated discounted price for group servicing
  Currently £175 for Air Source and £200 for Ground Source.
  cf for single installations: £220 for Air Source and £250 for Ground Source

## Slide 15: Adding Air to Air for an extension: - avoids more internal plumbing - rapid heating - runs off 13 amp socket

## Slide 16: Heat Pump for a New Build
Ruth Winterbottom

## Slide 17
New build 2 bedroom semi-detached bungalow, 2022
5.5kw solar array, 12.8kwh battery storage
Wanted an air-to-water heat pump, refused by everyone we approached, locally or nationally - air-to-air not mentioned by anyone at the time.
In order to go completely electric, we opted for ceiling-mounted infra-red panels.
Because of favourable tariffs/solar panels/batteries, 2025-26 bills £200

## Slide 18
Hottest days in summer overheated south-facing kitchen and workroom (bedroom 2) so thinking of heat pump air conditioning (air-to-air)
Fitted in February 2026, kWh usage falling already!